## Slide 1: ECE3056A: Architecture, Concurrency, Energy Lecture : Control Flow Handling
Prof. Moinuddin K. Qureshi
Slides Adapted from Prof. Onur Mutlu (CMU)

## Slide 2: Control Dependence
Question: What should the fetch PC be in the next cycle?
Answer: The address of the next instruction
  All instructions are control dependent on previous ones. Why?
If the fetched instruction is a non-control-flow instruction:
  Next Fetch PC is the address of the next-sequential instruction
  Easy to determine if we know the size of the fetched instruction
If the instruction that is fetched is a control-flow instruction:
  How do we determine the next Fetch PC?
In fact, how do we know whether or not the fetched instruction is a control-flow instruction?

## Slide 3: Branch Types
Type | Direction at fetch time | Number of possible next fetch addresses? | When is next fetch address resolved?
Conditional | Unknown | 2 | Execution (register dependent)
Unconditional | Always taken | 1 | Decode (PC + offset)
Call | Always taken | 1 | Decode (PC + offset)
Return | Always taken | Many | Execution (register dependent)
Indirect | Always taken | Many | Execution (register dependent)
Different branch types can be handled differently

## Slide 4: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions. Potential solutions:
If the instruction is a control-flow instruction:
  Stall the pipeline until we know the next fetch address
  Guess the next fetch address. How?
Employ delayed branching (branch delay slot)
Do something else (multithreading, covered later)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 5: Delayed Branching (I)
Change the semantics of a branch instruction
  Branch after N instructions
  Branch after N cycles
Idea: Delay the execution of a branch. N instructions (delay slots) that come after the branch are always executed regardless of branch direction.
Problem: How do you find instructions to fill the delay slots?
  Branch must be independent of delay slot instructions
Unconditional branch: Easier to find instructions to fill the delay slot
Conditional branch: Condition computation should not depend on instructions in delay slots  difficult to fill the delay slot

## Slide 6: Delayed Branching (II)
A
B
C
BR X
D
E
F
F
E
A
A
B
B
C
C
BR
BR
G
X:
--
A
B
C
BR X
D
E
F
G
X:
F
E
A
A
C
C
BR
BR
B
B
G
--
G
Normal code:
Timeline:
Delayed branch code:
Timeline:
6 cycles
5 cycles

## Slide 7: Delayed Branching (IV)
Advantages:
+ Keeps the pipeline full with useful instructions in a simple way assuming
1. Number of delay slots == number of instructions to keep the pipeline full before the branch resolves
2. All delay slots can be filled with useful instructions
Disadvantages:
  -- Not easy to fill the delay slots (even with a 2-stage pipeline)
  1. Number of delay slots increases with pipeline depth, superscalar execution width
  2. Number of delay slots should be variable with variable latency operations. Why?
-- Ties ISA semantics to hardware implementation
-- SPARC, MIPS, HP-PA: 1 delay slot
-- What if pipeline implementation changes with the next design?

## Slide 8: Branch Prediction: Guess the Next Instruction to Fetch
0x0004
0x0005
0x0006
0x0007
0x0008
I-$
RF
LD R1, MEM[R0]
ADD R2, R2, #1
0x0001
BRZERO 0x0001
0x0002
0x0003
DEC
ADD R3, R2, #1
0x0004
LD R2, MEM[R2]
MUL R1, R2, R3
0x0005
0x0006
LD R0, MEM[R2]
0x0007
12 cycles
8 cycles
D-$
PC
??
Branch prediction
WB

## Slide 9: Misprediction Penalty
LD R0, MEM[R2]
LD R2, MEM[R2]
BRZERO 0x0001
I-$
RF
LD R1, MEM[R0]
ADD R2, R2, #1
ADD R3, R2, #1
0x0001
0x0002
0x0003
0x0004
MUL R1, R2, R3
0x0005
0x0006
Flush!!
0x0007
0x0003
0x0004
0x0005
0x0006
0x0007
D-$
PC
DEC
WB

## Slide 10: Branch Prediction
Fetch Decode Rename Schedule RegisterRead Execute
Target Misprediction Detected! Flush the pipeline
Pipeline
A
B3
B1
D
E
F
A
B1
A
B1
A
D
B1
A
D
E
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B1
A
D
E
F
B3
What to fetch next?
Fetch from the correct target
Processors are pipelined to increase concurrency
How do we keep the pipeline full in the presence of branches?
  Guess the next instruction when a branch is fetched
  Requires guessing the direction and target of a branch
Branch condition, TARGET
Verify the Prediction

## Slide 11: Branch Prediction (Enhanced)
Idea: Predict the next fetch address (to be used in the next cycle)
Requires three things to be predicted:
  Whether the fetched instruction is a branch
  (Conditional) branch direction
  Branch target address (if taken)
Target addresses remain the same for conditional direct branches across dynamic instances
  Idea: Store the target address from previous instance and access it with the PC
  Called Branch Target Buffer (BTB) or Branch Target Address Cache

## Slide 12: Fetch Stage with BTB and Direction Prediction
target address
Direction predictor (2-bit counters)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current branch

## Slide 13: Simple Branch Direction Prediction Schemes
Compile time (static)
  Always not taken
  Always taken
  BTFN (Backward taken, forward not taken)
  Profile based (likely direction)
Run time (dynamic)
  Last time prediction (single-bit)

## Slide 14: Static Branch Prediction (I)
Always not-taken
  Simple to implement: no need for BTB, no direction prediction
  Low accuracy: ~40%
  Compiler can layout code such that the likely path is the “not-taken” path
Always taken
  No direction prediction
  Better accuracy: ~60%
    Backward branches (i.e. loop branches) are usually taken
    Backward branch: target address lower than branch PC
Backward taken, forward not taken (BTFN)
  Predict backward (loop) branches as taken, others not-taken

## Slide 15: Static Branch Prediction (II)
Profile-based
  Idea: Compiler determines likely direction for each branch using profile run. Encodes that direction as a hint bit in the branch instruction format.
+ Per branch prediction (more accurate than schemes in previous slide)
-- Requires hint bits in the branch instruction format
-- Accuracy depends on dynamic branch behavior:
TTTTTTTTTTNNNNNNNNNN  50% accuracy TNTNTNTNTNTNTNTNTNTN  50% accuracy
-- Accuracy depends on the representativeness of profile input set

## Slide 16: Dynamic Branch Prediction
Idea: Predict branches based on dynamic information (collected at run-time)
Advantages
  + No need for profiling: input set representativeness problem goes away
  + Prediction based on history of the execution of branches
  + It can adapt to dynamic changes in branch behavior
Disadvantages
  -- More complex (requires additional hardware)

## Slide 17: Last Time Predictor
Last time predictor
  Single bit per branch (stored in BTB)
  Indicates which direction branch went last time it executed
  TTTTTTTTTTNNNNNNNNNN  90% accuracy
Always mispredicts the last iteration and the first iteration of a loop branch
  Accuracy for a loop with N iterations = (N-2)/N
+ Loop branches for loops with large number of iterations
-- Loop branches for loops will small number of iterations
TNTNTNTNTNTNTNTNTNTN  0% accuracy
Last-time predictor CPI = [ 1 + (0.20*0.15) * 3 ] = 1.09 (Assuming 85% accuracy)

## Slide 18: Implementing the Last-Time Predictor
BTB
BTB idx
N-bit
tag
table
1 0
PC+2
nextPC
=
The 1-bit BHT (Branch History Table) entry is updated with the correct outcome after each execution of a branch
tag
One
Bit
Per
branch
taken?

## Slide 19: State Machine for Last-Time Prediction
predict
taken
predict
not
taken
actually
not taken
actually
taken
actually
taken
actually
not taken

## Slide 20: Improving the Last Time Predictor
Problem: A last-time predictor changes its prediction from TNT or NTT too quickly
  even though the branch may be mostly taken or mostly not taken
Solution Idea: Add hysteresis to the predictor so that prediction does not change on a single different outcome
  Use two bits to track the history of predictions for a branch instead of a single bit
  Can have 2 states for T or NT instead of 1 state for each
Smith, “A Study of Branch Prediction Strategies,” ISCA 1981.

## Slide 21: Two-Bit Counter Based Prediction
Each branch associated with a two-bit counter
One more bit provides hysteresis
A strong prediction does not change with one single different outcome
  Accuracy for a loop with N iterations = (N-1)/N
  TNTNTNTNTNTNTNTNTNTN  50% accuracy
  (assuming init to weakly taken)
  + Better prediction accuracy
  -- More hardware cost (but counter can be part of a BTB entry)
2BC predictor CPI = [ 1 + (0.20*0.10) * 3 ] = 1.06 (90% accuracy)

## Slide 22: State Machine for 2-bit Saturating Counter
Counter using saturating arithmetic
  There is a symbol for maximum and minimum values
pred
taken
11
pred
taken
10
pred
!taken
01
pred
!taken
00
actually
taken
actually
taken
actually
!taken
actually
!taken
actually
!taken
actually
!taken
actually
taken
actually
taken
“strongly
taken”
“weakly
taken”
“strongly
not taken”
“weakly
Not taken”

## Slide 23: Announcements
Midterm on Monday (BYOC: Bring your own calculator)
Review Session on Sunday (4:30-6pm in Regular Class)
Extra Office hours from me and TAs
  Me: Thursday, Friday 2-5pm (No office hours today)
  TAs: Will be posted on Piazza
Home work 1 due on Saturday 6pm
  This will take ~8-10 hours (so start early)
  It will require thinking, and applying concepts learned in class