## Slide 1: ECE3056A Architecture, Concurrency, and Energy Lecture: ISA Tradeoffs
Prof. Moinuddin K. Qureshi
NO OPEN LAPTOP OR TABLETS
Adapted from Slides of Prof. Mutlu (CMU)

## Slide 2
Updates: Recitation Section
Sanjay Kariyappa
skariyappa3@gatech.edu
Ivan Walker
ivanwalker14@gmail.com
Tu & Th 10:30-11:30
(Next to KACB 2332)
M & W 3:00-4:00
(Next to KACB 2332)
Recitation Section
Tue 6-7, Mason111 Room 1113
Recitation Section
Tue 6-7, Mason 111 Room 2117
Vinson will be helping with development of Labs & Grading.
His office hours only during the week when labs are due.

## Slide 3
What is a Recitation Section Anyway?
Source:http://web.mit.edu/uaap/learning/lectures/recitations.html

## Slide 4
Updates: Lab 1 Graded
Lab1 is graded, scores will released shortly.
We added extra test cases
For many students: All the test cases we provided pass, but
most of the new test cases fail  Lower Score
Importance of testing your code: The test cases we provide are necessary but not sufficient to get the functionality right
There will be a regrade opportunity (more details soon) 
Score = Avg(OldScore,NewScore)

## Slide 5
Extra Credit Problem (1% of grade)
Given that LC-3b does not have a MUL instruction we want to develop a routine that can perform MUL operations. The routine should take two operands of 8-bits each, available at locations 0x4000 and 0x4001 and should return the 16-bit resulting value at location 0x4002.

## Slide 6
Extra Credit: Due on Sept 2, 11:59pm
You will need to test your MUL routine for the following ten test cases, and report the computed answer and number of instructions for each test case. You will get points ONLY IF your program computes the correct results for ALL the ten test cases. Submit your .asm file along with a text file with the following table and line filled out.
Val 0x4000 | 0xFF | 0x00 | 0x00 | 0xFF | 0xFF | 0x01 | 0x12 | 0x64 | 0xAA | 0x96
Val 0x4001 | 0xFF | 0x00 | 0xFF | 0x00 | 0x01 | 0xFF | 0x34 | 0x64 | 0x55 | 0x69
Result at 0x4002 |  |  |  |  |  |  |  |  |  | 
Num Inst |  |  |  |  |  |  |  |  |  | 
The average number of instructions to perform MUL is: _____

## Slide 7: ISA: Architecture State, Instruction Format, Processing Model, Memory Model, …

## Slide 8: Many Different ISAs Over Decades
x86
PDP-x: Programmed Data Processor (PDP-11)
VAX
IBM 360
CDC 6600
SIMD ISAs: CRAY-1, Connection Machine
VLIW ISAs: Multiflow, Cydrome, IA-64 (EPIC)
PowerPC, POWER
RISC ISAs: Alpha, MIPS, SPARC, ARM
What are the fundamental differences?
  E.g., how instructions are specified and what they do
  E.g., how complex are the instructions

## Slide 9: Element of ISA
Instruction sequencing model
  Control flow vs. data flow
Instruction processing style
  Specifies the number of “operands” an instruction “operates” on and how it does so
  0, 1, 2, 3 address machines
    0-address: stack machine (push A, pop A, op)
    1-address: accumulator machine (ld A, st A, op A)
    2-address: 2-operand machine (one is both source and dest)
    3-address: 3-operand machine (source and dest are separate)
  Tradeoffs?
  Larger instructions vs. more executed operations
    Code size vs. execution time

## Slide 10: Examples
PDP-11: A 2-address machine
  PDP-11 ADD: 4-bit opcode, 2 6-bit operand specifiers
  Why? Limited bits to specify an instruction
  Disadvantage: One source operand is always clobbered with the result of the instruction
    How do you ensure you preserve the old value of the source?
X86: A 2-address (memory/memory) machine
Alpha: A 3-address (load/store) machine
MIPS? LC-3b?

## Slide 11: What Are the Elements of An ISA?
Instructions
  Opcode
  Operand specifiers (addressing modes)
    How to obtain the operand?
Data types
  Definition: Representation of information for which there are instructions that operate on the representation
  Integer, floating point, character, binary, decimal, BCD
  Doubly linked list, queue, string, bit vector, stack
    VAX: INSQUEUE and REMQUEUE instructions on a doubly linked list or queue; FINDFIRST
    Digital Equipment Corp., “VAX11 780 Architecture Handbook,” 1977-78.
    X86: SCAN opcode operates on character strings; PUSH/POP
Why are there different addressing modes?

## Slide 12: Data Type Tradeoffs
What is the benefit of having more or high-level data types in the ISA?
What is the disadvantage?
Think compiler/programmer vs. microarchitect
Concept of semantic gap
  Data types coupled tightly to the semantic level, or complexity of instructions
Early RISC architectures vs. Intel 432
  Early RISC: Only integer data type
  Intel 432: Object data type

## Slide 13: What Are the Elements of An ISA?
Registers
  How many
  Size of each register
Why is having registers a good idea?
  Concept of locality of data
  A recently produced/accessed value is likely to be used more than once (temporal locality)
    Storing that value in a register eliminate the need to go to memory each time that value is needed

## Slide 14: ISA-level Tradeoffs: Number of Registers
Affects:
  Number of bits used for encoding register address
  Number of values kept in fast storage (register file)
  (uarch) Size, access time, power consumption of register file
Large number of registers:
  + Enables better register allocation (and optimizations) by compiler  fewer saves/restores
  -- Larger instruction size
  -- Larger register file size

## Slide 15: What Are the Elements of An ISA?
Memory organization
  Address space: How many uniquely identifiable locations in memory
  Addressability: How much data does each uniquely identifiable location store
    Byte addressable: most ISAs, characters are 8 bits
    Bit addressable: Burroughs 1700.
    64-bit addressable: Some supercomputers. Why?
    32-bit addressable: First Alpha
    Food for thought
      How do you add 2 32-bit numbers with only byte addressability?
      How do you add 2 8-bit numbers with only 32-bit addressability?
      Big endian vs. little endian? MSB at low or high byte.

## Slide 16: Instruction Classes
Operate instructions
  Process data: arithmetic and logical operations
  Fetch operands, compute result, store result
  Implicit sequential control flow
Data movement instructions
  Move data between memory, registers, I/O devices
  Implicit sequential control flow
Control flow instructions
  Change the sequence of instructions that are executed

## Slide 17: What Are the Elements of An ISA?
Load/store vs. memory/memory architectures
  Load/store architecture: operate instructions operate only on registers
    E.g., MIPS, ARM and many RISC ISAs
  Memory/memory architecture: operate instructions can operate on memory locations
    E.g., x86, VAX and many CISC ISAs

## Slide 18: What Are the Elements of An ISA?
Addressing modes specify how to obtain the operands
  Absolute LW rt, 10000
  use immediate value as address
  Register Indirect: LW rt, (rbase)
  use GPR[rbase] as address
  Displaced or based: LW rt, offset(rbase)
  use offset+GPR[rbase] as address
  Indexed: LW rt, (rbase, rindex)
  use GPR[rbase]+GPR[rindex] as address
  Memory Indirect LW rt ((rbase))
  use value at M[ GPR[ rbase ] ] as address
  Auto inc/decrement LW Rt, (rbase)
  use GRP[rbase] as address, but inc. or dec. GPR[rbase] each time
Notes: Indexed mode for gather scatter.

## Slide 19: What Are the Benefits of Different Addressing Modes?
Another example of programmer vs. microarchitect tradeoff
Advantage of more addressing modes:
  Enables better mapping of high-level constructs to the machine: some accesses are better expressed with a different mode  reduced number of instructions and code size
    Think array accesses (autoincrement mode)
    Think indirection (pointer chasing)
    Sparse matrix accesses
Disadvantage:
  More work for the compiler
  More work for the microarchitect

## Slide 20: X86 SIB-D Addressing Mode
x86 Manual Vol. 1, page 3-31

## Slide 21: X86 Manual: Suggested Uses of Addressing Modes
x86 Manual Vol. 1, page 3-32

## Slide 22: What Are the Elements of An ISA?
How to interface with I/O devices
  Memory mapped I/O
    A region of memory is mapped to I/O devices
    I/O operations are loads and stores to those locations
  Special I/O instructions
    IN and OUT instructions in x86 deal with ports of the chip

## Slide 23: What Are the Elements of An ISA?
Privilege modes
  User vs supervisor
  Who can execute what instructions?
Exception and interrupt handling
  What procedure is followed when something goes wrong with an instruction?
  What procedure is followed when an external device requests the processor?
Virtual memory
  Each program has the illusion of the entire memory space, which is greater than physical memory
Access protection
We will talk about these later
Notes: MIPS started out without having interrupt vectors… When an interrupt happens, SW figured out who interrupted… Costly in terms of time…

## Slide 24: Complex vs. Simple ISA: Tradeoffs The (in)famous RISC vs CISC battle !

## Slide 25: Complex vs. Simple Instructions
Complex instruction: An instruction does a lot of work, e.g. many operations
  Insert in a doubly linked list
  Compute FFT
  String copy
Simple instruction: An instruction does small amount of work, it is a primitive
  Add
  XOR
  Shift

## Slide 26: Complex vs. Simple Instructions
Advantages of Complex instructions
  + Denser encoding  smaller code size  better memory utilization, saves off-chip bandwidth, better cache hit rate (better packing of instructions)
  + Simpler compiler: no need to optimize small instructions as much
Disadvantages of Complex Instructions
  - Larger chunks of work  compiler has less opportunity to optimize
  - More complex hardware  translation from a high level to control signals and optimization needs to be done by hardware
  - Compiler is limited in fine-grained optimizations it can do

## Slide 27: ISA-level Tradeoffs: Semantic Gap
Some tradeoffs (for you to think about)
Simple compiler, complex hardware vs. complex compiler, simple hardware
  Caveat: Translation (indirection) can change the tradeoff!
Burden of backward compatibility
Performance?
  Optimization opportunity: Example of VAX INDEX instruction: who (compiler vs. hardware) puts more effort into optimization?
  Instruction size, code size

## Slide 28: X86: Small Semantic Gap: String Operations
An instruction operates on a string
  Move one string of arbitrary length to another location
  Compare two strings
Enabled by the ability to specify repeated execution of an instruction (in the ISA)
  Using a “prefix” called REP prefix
Example: REP MOVS instruction
  Only two bytes: REP prefix byte and MOVS opcode byte (F2 A4)
  Implicit source and destination registers pointing to the two strings (ESI, EDI)
  Implicit count register (ECX) specifies how long the string is

## Slide 29: X86: Small Semantic Gap: String Operations
REP MOVS (DEST SRC)
How many instructions does this take in MIPS?

## Slide 30: Small Semantic Gap Examples in VAX
FIND FIRST
  Find the first set bit in a bit field
  Helps OS resource allocation operations
SAVE CONTEXT, LOAD CONTEXT
  Special context switching instructions
INSQUEUE, REMQUEUE
  Operations on doubly linked list
INDEX
  Array access with bounds checking
STRING Operations
  Compare strings, find substrings, …
Cyclic Redundancy Check Instruction
EDITPC
  Implements editing functions to display fixed format output
Digital Equipment Corp., “VAX11 780 Architecture Handbook,” 1977-78.

## Slide 31
Announcements
Lab1 re-grade and “Part B” test cases
Lab1ExtraCredit
  Check the Piazza announcement for byteadd example
  We will support only ecelinsrv machines [no mac/ubuntu/etc.]
  You can do MUL better than add N times (think!)
  Top 5 submissions with lowest inst count: extra 1% grade Let the competition begin
3. Lab2 will be up tomorrow: go through microarch slides and PDF
4. If you have trouble with VPN/SSH, attend recitation section or see one of the TAs during their office hours

## Slide 32: A Note on ISA Evolution
ISAs have evolved to reflect/satisfy the concerns of the day
Examples:
  Limited memory size
  Limited compiler optimization technology
  Limited memory bandwidth
  Need for specialization in important applications (e.g., MMX)

## Slide 33: Effect of Translation
One can translate from one ISA to another ISA to change the semantic gap tradeoffs
Examples
  Intel’s and AMD’s x86 implementations translate x86 instructions into programmer-invisible microoperations (simple instructions) in hardware
  Transmeta’s x86 implementations translated x86 instructions into “secret” VLIW instructions in software (code morphing software)
Think about the tradeoffs

## Slide 34: ISA-level Tradeoffs: Instruction Length
Fixed length: Length of all instructions the same
  + Easier to decode single instruction in hardware
  + Easier to decode multiple instructions concurrently
  -- Wasted bits in instructions (Why is this bad?)
  -- Harder-to-extend ISA (how to add new instructions?)
Variable length: Length of instructions different (determined by opcode and sub-opcode)
    + Compact encoding (Why is this good?)
    Intel 432: Huffman encoding (sort of). 6 to 321 bit instructions. How?
    -- More logic to decode a single instruction
    -- Harder to decode multiple instructions concurrently
Tradeoffs
  Code size (memory space, bandwidth, latency) vs. hardware complexity
  ISA extensibility and expressiveness
  Performance? Smaller code vs. imperfect decode
Notes: Huffman encoding: shorter strings for more commonly occurring instructions

## Slide 35: ISA-level Tradeoffs: Uniform Decode
Uniform decode: Same bits in each instruction correspond to the same meaning
  Opcode is always in the same location
  Ditto operand specifiers, immediate values, …
  Many “RISC” ISAs: Alpha, MIPS, SPARC
  + Easier decode, simpler hardware
  + Enables parallelism: generate target address before knowing the instruction is a branch
  -- Restricts instruction format (fewer instructions?) or wastes space
Non-uniform decode
  E.g., opcode can be the 1st-7th byte in x86
  + More compact and powerful instruction format
  -- More complex decode logic

## Slide 36: x86 vs. Alpha Instruction Formats
x86:
Alpha:

## Slide 37: MIPS Instruction Format
R-type, 3 register operands
I-type, 2 register operands and 16-bit immediate operand
J-type, 26-bit immediate operand
Simple Decoding
  4 bytes per instruction, regardless of format
  must be 4-byte aligned (2 lsb of PC must be 2b’00)
  format and fields easy to extract in hardware
R-type
0
6-bit
rs
5-bit
rt
5-bit
rd
5-bit
shamt
5-bit
funct
6-bit
opcode
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
I-type
opcode
6-bit
immediate
26-bit
J-type

## Slide 38: MIPS: Aligned Access
LW/SW alignment restriction: 4-byte word-alignment
  not designed to fetch memory bytes not within a word boundary
  not designed to rotate unaligned bytes into registers
Need more instructions for the “infrequent” case
  LWL/LWR is slower
  Note LWL and LWR still fetch within word boundary
byte-3
byte-2
byte-1
byte-0
byte-7
byte-6
byte-5
byte-4
MSB
LSB
A
B
C
D
byte-6
byte-5
byte-4
D
byte-6
byte-5
byte-4
byte-3
LWL rd 6(r0) 
LWR rd 3(r0) 

## Slide 39: X86: Unaligned Access
LD/ST instructions automatically align data that spans a “word” boundary
Programmer/compiler does not need to worry about where data is stored (whether or not in a word-aligned location)

## Slide 40: X86: Unaligned Access

## Slide 41: Review: ISA Tradeoffs
Complex vs. simple instructions: concept of semantic gap
Use of translation to change the tradeoffs
Fixed vs. variable length, uniform vs. non-uniform decode
Number of registers, addressing modes
Unaligned memory access
What is the benefit of translating complex instructions to “simple instructions” before executing them?
  In hardware (a la Intel, AMD)?
  In software (a la Transmeta)?
Which ISA is easier to extend: fixed length or variable length?

## Slide 42: A Note on Length and Uniformity
Uniform decode usually goes with fixed length
In a variable length ISA, uniform decode can be a property of instructions of the same length
  It is hard to think of it as a property of instructions of different lengths

## Slide 43: A Note on RISC vs. CISC
Usually, …
RISC
  Simple instructions
  Fixed length
  Uniform decode
  Few addressing modes
CISC
  Complex instructions
  Variable length
  Non-uniform decode
  Many addressing modes