## Slide 1: LC3b ISA
Moinuddin K Qureshi
[REMINDER: No OPEN Laptops/Tablets/etc.]

## Slide 2: What is A Computer?
We will cover all three components
Memory
(program
and data)
I/O
Processing
control
(sequencing)
datapath

## Slide 3: The Von Neumann Model/Architecture
Also called stored program computer (instructions in memory). Two key properties:
Stored program
  Instructions stored in a linear memory array
  Memory is unified between instructions and data
    The interpretation of a stored value depends on the control signals
Sequential instruction processing
  One instruction processed (fetched, executed, and completed) at a time
  Program counter (instruction pointer) identifies the current instr.
  Program counter is advanced sequentially except for control transfer instructions
When is a value interpreted as an instruction?

## Slide 4: The Von-Neumann Model
All major instruction set architectures today use this model
  x86, MIPS, SPARC, Alpha, ARM, POWER
Underneath (at the microarchitecture level), the execution model of almost all implementations (or, microarchitectures) is very different
  Pipelined instruction execution: Intel 80486 uarch
  Multiple instructions at a time: Intel Pentium uarch
  Out-of-order execution: Intel Pentium Pro uarch
  Separate instruction and data caches
But, what happens underneath that is not consistent with the von Neumann model is not exposed to software
  Difference between ISA and microarchitecture

## Slide 5: ISA vs. Microarchitecture
ISA
  Agreed upon interface between software and hardware
    SW/compiler assumes, HW promises
  What the software writer needs to know to write and debug system/user programs
Microarchitecture
  Specific implementation of an ISA
  Not visible to the software
Microprocessor
  ISA, uarch, circuits
  “Architecture” = ISA + microarchitecture
Microarchitecture
ISA
Program
Algorithm
Problem
Circuits
Electrons
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.
Builder/user interface

## Slide 6: ISA vs. Microarchitecture
What is part of ISA vs. Uarch?
  Gas pedal: interface for “acceleration”
  Internals of the engine: implements “acceleration”
Implementation (uarch) can be various as long as it satisfies the specification (ISA)
  Add instruction vs. Adder implementation
    Bit serial, ripple carry, carry lookahead adders are all part of microarchitecture
  x86 ISA has many implementations: 286, 386, 486, Pentium, Pentium Pro, …
Microarchitecture usually changes faster than ISA
  Few ISAs (x86, SPARC, MIPS, Alpha) but many uarchs
  Why?

## Slide 7: Property of ISA vs. Uarch?
ADD instruction’s opcode
Number of general purpose registers
Number of ports to the register file
Number of cycles to execute the MUL instruction
Whether or not the machine employs pipelined instruction execution
Remember
  Microarchitecture: Implementation of the ISA under specific design constraints and goals

## Slide 8: Overview of LC-3b ISA
8 REGS
R0-R7
(16 bit wide)
216 bytes
0x0000
To
0xFFFF
PC
PSR
Memory
16-bit INSTRUCTIONS (4-bit opcode, 14 defined+ 2 reserved)
Condition codes

## Slide 9: Arithmetic & Logic Instructions

## Slide 14: Memory Instructions

## Slide 19: Control Flow Instructions

## Slide 25: LEA: Get Address in Register

## Slide 26
Note: this instruction does not access memory.
It is more like ALU op rather than memory op.

## Slide 27
Concept of “Bit Steering”
  A bit in the instruction determines
  the interpretation of other bits.
  Which instructions employ Bit steering?

## Slide 28
A Day in the Life of an LC-3b Instruction
0x0000
R0
0x1111
R1
0x2222
R2
0x3333
R3
0x4444
R4
0x5555
R5
0x6666
R6
0x7777
R7
0x1234
PC
0
N
1
Z
0
P
0x42
0x1234
0x10
0x1235
0xFF
0x1236
0x1E
0x1237
0x7F
0x1238
0x92
0x1239
0x11
0x123A
0x11
0x123B
0x11
0x123C
0x11
0x123D
0x11
0x123E
0x11
0x123F
0x11
0x1240
ooo
ooo

## Slide 29
1. What happens with this instruction ?
R0
0x1111
R1
0x2222
R2
0x3333
R3
0x4444
R4
0x5555
R5
0x6666
R6
0x7777
R7
0x1234
PC
0
N
1
Z
0
P
0x42
0x1234
0x10
0x0000
0x1235
0xFF
0x1236
0x1E
0x1237
0x7F
0x1238
0x92
0x1239
0x11
0x123A
0x11
0x123B
0x11
0x123C
0x11
0x123D
0x11
0x123E
0x11
0x123F
0x11
0x1240
ooo
ooo
Inst Fetched: 0x1042
0001 0000 0100 0010
0001 0000 0100 0010
ADD R0, R1, R2
0x1236
0
1
0x3333

## Slide 30
2. What happens with this instruction ?
R0
0x1111
R1
0x2222
R2
0x3333
R3
0x4444
R4
0x5555
R5
0x6666
R6
0x7777
R7
0x1236
PC
0
N
0
Z
1
P
0x42
0x1234
0x10
0x3333
0x1235
0xFF
0x1236
0x1E
0x1237
0x7F
0x1238
0x92
0x1239
0x11
0x123A
0x11
0x123B
0x11
0x123C
0x11
0x123D
0x11
0x123E
0x11
0x123F
0x11
0x1240
ooo
ooo
Inst Fetched: 0x1EFF
0001 1110 1111 1111
0001 1110 1111 1111
ADD R7, R3, #-1
0x1238
1
0x3332

## Slide 31
3. What happens with this instruction ?
R0
0x1111
R1
0x2222
R2
0x3333
R3
0x4444
R4
0x5555
R5
0x6666
R6
0x3332
R7
0x1238
PC
0
N
0
Z
1
P
0x42
0x1234
0x10
0x3333
0x1235
0xFF
0x1236
0x1E
0x1237
0x7F
0x1238
0x92
0x1239
0x11
0x123A
0x11
0x123B
0x11
0x123C
0x11
0x123D
0x11
0x123E
0x11
0x123F
0x11
0x1240
ooo
ooo
Inst Fetched: 0x927F
1001 0010 0111 1111
1001 0010 0111 1111
XOR R1, R1, #-1
0x123A
1
0xEEEE
0