## Slide 1: Pipeline Dependencies
Moinuddin K Qureshi

## Slide 2
Announcements
Homework 1 posted (due Saturday 6pm, 2 pts for submission)
Midterm 1 is scheduled for next Monday (20% of course grade)
Three pages of notes allowed (both sides, page size as big as you want, but these sheets MUST be filled in your own handwriting)
Test of understanding, not memorization
Be prepared to see problems that may not be similar to practice problems (Engineering is about applying known concepts to unknown problems)
I will hold an (optional) review session on Sunday evening
TAs will have extra office hours this week. Also the recitation section tomorrow can provide help with midterm preparation and HW1

## Slide 3
“Electronic Etiquette Policy” for this Class
No open Laptops, Tablets, Phone etc. in lectures.
Why? Several studies [Princeton and U California] show Open Laptops are a hindrance to classroom learning: test scores of students with open
Laptop substantially lower than the students with closed screens
http://www.newyorker.com/tech/elements/the-case-for-banning-laptops-in-the-classroom (6/6/2014)
The open screens affects:
You (hard to be a part of the discussion if your attention is on your screen)
Your fellow students (who may get distracted by your videos of cute kittens)
Professor (more motivated if students are paying attention)
If your screens/texting causes trouble for other students in class, I may have to ask you to leave and return after taking care of what you need to.

## Slide 4
Basic Five Stage Pipeline
Fetch
Dec
Exec
Mem
WB
Reg
File

## Slide 5: No Data Dependencies
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B | A |  | 
4 | D | C | B | A | 
5 | E | D | C | B | A
6 | F | E | D | C | B
7 | G | F | E | D | C
8 | H | G | F | E | D
Assume a program where all instructions (A-H) are independent

## Slide 6: Data Dependencies
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B (R2?) | A |  | 
4 | C | B (R2?) |  | A | 
5 | C | B (R2?) |  |  | A(R2,end)
6 | C | B (R2) |  |  | 
7 |  | C | B |  | 
8 |  |  | C | B | 
9 |  |  |  | C | B
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
Reg
File

## Slide 7: Forwarding (nominal)
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B (R2?) | A |  | 
4 | C | B (R2?) |  | A | 
5 | C | B (R2) |  |  | A(R2OK)
6 |  |  | B |  | 
7 |  |  | C | B | 
8 |  |  |  | C | B
9 |  |  |  |  | C
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
Reg
File
MUX

## Slide 8: Forwarding (all stages)
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
Reg
File
MUX

## Slide 9: Forwarding (all stages)
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B | A |  |  | 
3 | C | B (R2) | A(Bypass) |  | 
4 |  | C | B | A | 
5 |  |  | C | B | A
6 |  |  |  | C | B
7 |  |  |  |  | C
8 |  |  |  |  | 
9 |  |  |  |  | 
A: ADD R2, R1, R0
B: ADD R3, R2, R0
C: ADD R7, R5, R4

## Slide 10: What about Control Dependency?
Cycle Num | FETCH | DECODE | EXECUTE | MEMORY | WBACK
1 | A |  |  |  | 
2 | B (stall) | A |  |  | 
3 | B (stall) |  | A |  | 
4 | B (stall) |  |  | A (PC OK) | 
5 | C |  |  |  | A
6 |  | C |  |  | 
7 |  |  | C |  | 
8 |  |  |  | C | 
9 |  |  |  |  | C
A: BR nzp, C
B: ADD R3,R3, #5
C: ADD R7, R5, R4
Fetch
Dec
Exec
Mem
WB
PC

## Slide 11: Why is this an important bottleneck?
On average, 20% of the instructions are control flow (branches)
Lets assume a machine with CPI=1
For 20% of instructions, we have add three cycles of bubbles.
What is the net CPI?
Let there be 100 instructions, so perfect cycles=100
20 instructions @ 3 extra cycles = 60 cycles additional
Total cycles = 100+60 = 160  Net CPI is now 1.6
Slowdown of 60% !
Modern pipelines are 15-20 deep, so 12-16 bubbles per branch!
What can we do to mitigate this problem?