## Slide 1: ECE3056A Architecture, Concurrency, and Energy Lecture: Pipelined Microarchitectures
Prof. Moinuddin Qureshi
Slides adapted from: Prof. Mutlu (CMU)

## Slide 2: The Laundry Analogy
“place one dirty load of clothes in the washer”
“when the washer is finished, place the wet load in the dryer”
“when the dryer is finished, take out the dry load and fold”
“when folding is finished, ask your roommate (??) to put the clothes away”
- steps to do a load are sequentially dependent
- no dependence between different loads
- different steps do not share resources
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 3: Pipelining Multiple Loads of Laundry
- latency per load is the same
- throughput increased by 4
- 4 loads of laundry in parallel
- no additional resources
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 4: Can We Design Better Microarchitecture?
What limitations do you see with the multi-cycle design?
Limited concurrency
  Some hardware resources are idle during different phases of instruction processing cycle
  “Fetch” logic is idle when an instruction is being “decoded” or “executed”
  Most of the datapath is idle when a memory access is happening

## Slide 5: Can We Use the Idle Hardware to Improve Concurrency?
Goal: Concurrency  throughput (more “work” completed in one cycle)
Idea: When an instruction is using some resources in its processing phase, process other instructions on idle resources not needed by that instruction
  E.g., when an instruction is being decoded, fetch the next instruction
  E.g., when an instruction is being executed, decode another instruction
  E.g., when an instruction is accessing data memory (ld/st), execute the next instruction
  E.g., when an instruction is writing its result into the register file, access data memory for the next instruction

## Slide 6: Pipelining: Basic Idea
More systematically:
  Pipeline the execution of multiple instructions
  Analogy: “Assembly line processing” of instructions
Idea:
  Divide the instruction processing cycle into distinct “stages” of processing
  Ensure there are enough hardware resources to process one instruction in each stage
  Process a different instruction in each stage
    Instructions consecutive in program order are processed in consecutive stages
Benefit: Increases instruction processing throughput (1/CPI)
Downside: Start thinking about this…

## Slide 7: Example: Execution of Four Independent ADDs
Multi-cycle: 4 cycles per instruction
Pipelined: 4 cycles per 4 instructions (steady state)
Time
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
Time

## Slide 8: Pipelining Multiple Loads of Laundry: In Practice
the slowest step decides throughput
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 9: Pipelining Multiple Loads of Laundry: In Practice
A
B
A
B
Throughput restored (2 loads per hour) using 2 dryers
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 10: Ideal Pipelining
combinational logic (F,D,E,M,W)
T psec
BW=~(1/T)
BW=~(2/T)
T/2 ps (F,D,E)
T/2 ps (M,W)
BW=~(3/T)
T/3
ps (F,D)
T/3
ps (E,M)
T/3
ps (M,W)

## Slide 11: More Realistic Pipeline: Throughput
Nonpipelined version with delay T
BW = 1/(T+S) where S = latch delay
k-stage pipelined version
BWk-stage = 1 / (T/k +S )
BWmax = 1 / (1 gate delay + S )
T ps
T/k
ps
T/k
ps

## Slide 12: More Realistic Pipeline: Cost
Nonpipelined version with combinational cost G
Cost = G+L where L = latch cost
k-stage pipelined version
Costk-stage = G + Lk
G gates
G/k
G/K

## Slide 13: An Ideal Pipeline
Goal: Increase throughput with little increase in cost (hardware cost, in case of instruction processing)
Repetition of identical operations
  The same operation is repeated on a large number of different inputs
Repetition of independent operations
  No dependencies between repeated operations
Uniformly partitionable suboperations
  Processing an be evenly divided into uniform-latency suboperations (that do not share resources)
Good examples: automobile assembly line, doing laundry
  What about instruction processing pipeline?

## Slide 14: Instruction Pipeline: Not An Ideal Pipeline
Identical operations ... NOT!
 different instructions do not need all stages
    - Forcing different instructions to go through the same multi-function pipe
     external fragmentation (some pipe stages idle for some instructions)
Uniform suboperations ... NOT!
 difficult to balance the different pipeline stages
    - Not all pipeline stages do the same amount of work
     internal fragmentation (some pipe stages are too-fast but take the same clock cycle time)
Independent operations ... NOT!
 instructions are not independent of each other
    - Need to detect and resolve inter-instruction dependencies to ensure the pipeline operates correctly
     Pipeline is not always moving (it stalls)

## Slide 15: Issues in Pipeline Design
Balancing work in pipeline stages
  How many stages and what is done in each stage
Keeping the pipeline correct, moving, and full in the presence of events that disrupt pipeline flow
  Handling dependences
    Data
    Control
  Handling resource contention
  Handling long-latency (multi-cycle) operations
Handling exceptions, interrupts
Advanced: Improving pipeline throughput
  Minimizing stalls