## Slide 1: ECE3056A Architecture, Concurrency, and Energy Lecture: Pipelined Microarchitectures
Prof. Moinuddin Qureshi
Slides adapted from: Prof. Mutlu (CMU)

## Slide 2: The Laundry Analogy
“place one dirty load of clothes in the washer”
“when the washer is finished, place the wet load in the dryer”
“when the dryer is finished, take out the dry load and fold”
“when folding is finished, ask your roommate (??) to put the clothes away”
- steps to do a load are sequentially dependent
- no dependence between different loads
- different steps do not share resources
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 3: Pipelining Multiple Loads of Laundry
- latency per load is the same
- throughput increased by 4
- 4 loads of laundry in parallel
- no additional resources
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 4: Can We Design Better Microarchitecture?
What limitations do you see with the multi-cycle design?
Limited concurrency
  Some hardware resources are idle during different phases of instruction processing cycle
  “Fetch” logic is idle when an instruction is being “decoded” or “executed”
  Most of the datapath is idle when a memory access is happening

## Slide 5: Can We Use the Idle Hardware to Improve Concurrency?
Goal: Concurrency  throughput (more “work” completed in one cycle)
Idea: When an instruction is using some resources in its processing phase, process other instructions on idle resources not needed by that instruction
  E.g., when an instruction is being decoded, fetch the next instruction
  E.g., when an instruction is being executed, decode another instruction
  E.g., when an instruction is accessing data memory (ld/st), execute the next instruction
  E.g., when an instruction is writing its result into the register file, access data memory for the next instruction

## Slide 6: Pipelining: Basic Idea
More systematically:
  Pipeline the execution of multiple instructions
  Analogy: “Assembly line processing” of instructions
Idea:
  Divide the instruction processing cycle into distinct “stages” of processing
  Ensure there are enough hardware resources to process one instruction in each stage
  Process a different instruction in each stage
    Instructions consecutive in program order are processed in consecutive stages
Benefit: Increases instruction processing throughput (1/CPI)
Downside: Start thinking about this…

## Slide 7: Example: Execution of Four Independent ADDs
Multi-cycle: 4 cycles per instruction
Pipelined: 4 cycles per 4 instructions (steady state)
Time
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
Time

## Slide 8: Pipelining Multiple Loads of Laundry: In Practice
the slowest step decides throughput
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 9: Pipelining Multiple Loads of Laundry: In Practice
A
B
A
B
Throughput restored (2 loads per hour) using 2 dryers
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 10: Ideal Pipelining
combinational logic (F,D,E,M,W)
T psec
BW=~(1/T)
BW=~(2/T)
T/2 ps (F,D,E)
T/2 ps (M,W)
BW=~(3/T)
T/3
ps (F,D)
T/3
ps (E,M)
T/3
ps (M,W)

## Slide 11: More Realistic Pipeline: Throughput
Nonpipelined version with delay T
BW = 1/(T+S) where S = latch delay
k-stage pipelined version
BWk-stage = 1 / (T/k +S )
BWmax = 1 / (1 gate delay + S )
T ps
T/k
ps
T/k
ps

## Slide 12: More Realistic Pipeline: Cost
Nonpipelined version with combinational cost G
Cost = G+L where L = latch cost
k-stage pipelined version
Costk-stage = G + Lk
G gates
G/k
G/K

## Slide 13: An Ideal Pipeline
Goal: Increase throughput with little increase in cost (hardware cost, in case of instruction processing)
Repetition of identical operations
  The same operation is repeated on a large number of different inputs
Repetition of independent operations
  No dependencies between repeated operations
Uniformly partitionable suboperations
  Processing an be evenly divided into uniform-latency suboperations (that do not share resources)
Good examples: automobile assembly line, doing laundry
  What about instruction processing pipeline?

## Slide 14: Instruction Pipeline: Not An Ideal Pipeline
Identical operations ... NOT!
 different instructions do not need all stages
    - Forcing different instructions to go through the same multi-function pipe
     external fragmentation (some pipe stages idle for some instructions)
Uniform suboperations ... NOT!
 difficult to balance the different pipeline stages
    - Not all pipeline stages do the same amount of work
     internal fragmentation (some pipe stages are too-fast but take the same clock cycle time)
Independent operations ... NOT!
 instructions are not independent of each other
    - Need to detect and resolve inter-instruction dependencies to ensure the pipeline operates correctly
     Pipeline is not always moving (it stalls)

## Slide 15: Why Latches
Latches allow you to “checkpoint” the work done.
  Lets see what happens if you do not latch the work
LatchIN
LatchOUT
Assume each invertor takes exactly 0.5 ns.
What is the cycle time? What is the frequency?

## Slide 16: Why Latches?
What happens with pipeline
LatchIN
LatchOUT
Assume each invertor takes exactly 0.5 ns (latch time is negligible).
What is the cycle time? What is the frequency?
LatchMID
t=0ns
t=0.5ns
t=1.5ns
t=2ns
t=1ns
t=1ns

## Slide 17: Why Latches?
What happens if we take the mid latch out ?
LatchIN
LatchOUT
At 1 ns ? The line between second and third invertor?
LatchMID
t=0ns
t=0.5ns
t=1.5ns
t=2ns
t=1ns

## Slide 18: Why Latches?
What if the different paths of a pipeline are unbalanced?
LatchIN
LatchOUT
T=0ns
T=0.5ns
T=1ns
T=1.5ns
T=2ns

## Slide 19: Why Latches?
What if the different paths of a pipeline are unbalanced?
LatchIN
LatchOUT
T=0ns
T=0.5ns
T=2ns
LatchMID
t=1ns
T=1.5ns
T=1ns

## Slide 20: Why Latches?
What if the different paths of a pipeline are unbalanced?
Now, if we take the mid latch out ?
LatchIN
LatchOUT
T=0ns
T=0.5ns
T=2ns
LatchMID
t=1ns
t=1.5ns
Unbalanced paths can give garbage output at the Latch
Impractical/Expensive to balance all paths, think Full Adder (bit_0 of the full adder will arrive much earlier than bit_n)

## Slide 21: Issues in Pipeline Design
Balancing work in pipeline stages
  How many stages and what is done in each stage
Keeping the pipeline correct, moving, and full in the presence of events that disrupt pipeline flow
  Handling dependences
    Data
    Control
  Handling resource contention
  Handling long-latency (multi-cycle) operations
Handling exceptions, interrupts
Advanced: Improving pipeline throughput
  Minimizing stalls

## Slide 22: Causes of Pipeline Stalls
Resource contention
Dependences (between instructions)
  Data
  Control
Long-latency (multi-cycle) operations

## Slide 23: Dependences and Their Types
Also called “dependency” or “Hazard”
Dependencies dictate ordering requirements between instructions
Two types
  Data dependence
  Control dependence
Resource contention is sometimes called resource dependence
  However, this is not fundamental to (dictated by) program semantics, so we will treat it separately

## Slide 24: Handling Resource Contention
Happens when instructions in two pipeline stages need the same resource
Solution 1: Eliminate the cause of contention
  Duplicate the resource or increase its throughput
    E.g., use separate instruction and data memories (caches)
    E.g., use multiple ports for memory structures
Solution 2: Detect the resource contention and stall one of the contending stages
  Which stage do you stall?
  Example: What if you had a single read and write port for the register file?

## Slide 25: Data Dependences
Types of data dependences
  Flow dependence (true data dependence – read after write)
  Output dependence (write after write)
  Anti dependence (write after read)
Which ones cause stalls in a pipelined machine?
  For all of them, we need to ensure semantics of the program are correct
  Flow dependences always need to be obeyed because they constitute true dependence on a value
  Anti and output dependences exist due to limited number of architectural registers
    They are dependence on a name, not a value
    We will later see what we can do about them

## Slide 26: Data Dependence Types
Flow dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW)
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR)
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW)
      r3  r6 op r7

## Slide 27: How to Handle Data Dependences
Anti and output dependences are easier to handle
  write to the destination in one stage and in program order
Flow dependences are more interesting (and challenging)
Five fundamental ways of handling flow dependences
  Detect and stall
  Detect and forward/bypass data to dependent instruction
  Eliminate the need for detecting dependence at the software level
    Software-based interlocking: No need to detect
  Do something else (fine-grained multithreading)
    No need to detect
  Predict the needed values and execute “speculatively”

## Slide 28: RAW Dependence Handling
Following flow dependences lead to conflicts in the 5-stage pipeline
MEM
WB
IF
ID
IF
EX
ID
MEM
EX
WB
ADD R0, R1, R2
ADD r- ra R0
MEM
IF
ID
EX
IF
ID
EX
IF
ID
IF
ADD r- ra R0
ADD r- ra R0
ADD r- ra R0
ADD r- ra R0
?

## Slide 29: Interlocking
Detection of dependence between instructions in a pipelined processor to guarantee correct execution
Software based interlocking
vs.
Hardware based interlocking
Quiz: “MIPS” acronym?

## Slide 30: Approaches to Dependence Detection (I)
Scoreboarding
  Each register in register file has a Valid bit associated with it
  An instruction that is writing to the register resets the Valid bit
  An instruction in Decode stage checks if all its source and destination registers are Valid
    Yes: No need to stall… No dependence
    No: Stall the instruction
Advantage:
  Simple. 1 bit per register
Disadvantage:
  Need to stall for all types of dependences, not only flow dep.

## Slide 31: Approaches to Dependence Detection (II)
Combinational dependence check logic
  Special logic that checks if any instruction in later stages is supposed to write to any source register of the instruction that is being decoded
  Yes: stall the instruction/pipeline
  No: no need to stall… no flow dependence
Advantage:
  No need to stall on anti and output dependences
Disadvantage:
  Logic is more complex than a scoreboard
  Logic becomes more complex as we make the pipeline deeper and wider (superscalar)

## Slide 32: Data Forwarding (or Data Bypassing)
It is intuitive to think of RF as state
  “add rx ry rz” literally means get values from RF[ry] and RF[rz] respectively and put result in RF[rx]
But, RF is just a part of a computing abstraction
  “add rx ry rz” means 1. get the results of the last instructions to define the values of RF[ry] and RF[rz], respectively, and 2. until another instruction redefines RF[rx], younger instructions that refers to RF[rx] should use this instruction’s result
What matters is to maintain the correct “dataflow” between operations, thus
ID
ID
ID
IF
ID
WB
IF
ID
EX
MEM
add ra r- r-
addi r- ra r-
MEM
IF
EX
WB