## Slide 1: ECE3056A
Prof. Moinuddin Qureshi
Thanks to Prof. Kim, Prof. Loh, Prof. Pruvulovic for earlier versions of the lecture notes!

## Slide 2: Memory Hierarchy
Memory: Just an “ocean of bits”
IDEAL Memory: Zero cost, zero latency, infinite capacity
Trade-off between: latency and capacity (big is slow)
Trade-off between cost: fast is typically expensive
Solution: Build a hierarchy (frequent: fast, else: slow, cheap)

## Slide 3: Memory Hierarchy
Registers
On-Chip
SRAM
Off-Chip
SRAM
DRAM
Flash/Disk
CAPACITY
SPEED and COST

## Slide 4: Types of Memory
Type | Size | Speed | Cost/bit
Register | < 1KB | < 1ns | $$$$
On-chip SRAM | 8KB-6MB | < 10ns | $$$
Off-chip SRAM | 1Mb – 16Mb | < 20ns | $$
DRAM | 64MB – 1TB | < 100ns | $
Flash | 64MB – 32GB | < 100us | c
Disk | 40GB – 1PB | < 20ms | ~0

## Slide 5: Locality and Caches
Data Locality
  Temporal: if data item needed now, it is likely to be needed again in near future
  Spatial: if data item needed now, nearby data likely to be needed in near future
Exploiting Locality: Caches
  Keep recently used data in fast memory close to the processor
  Also bring nearby data there

## Slide 6: Memory Latency is Long
60-100ns not uncommon
Quick back-of-the-envelope calculation:
  2GHz CPU
   0.5ns / cycle
  100ns memory  200 cycle memory latency!
Solution: Caches

## Slide 7: Cache Basics
Fast (but small) memory close to processor
When data referenced
  If in cache, use cache instead of memory
  If not in cache, bring into cache (actually, bring entire block of data, too)
  Maybe have to kick something else out to do it!
Important decisions
  Placement: where in the cache can a block go?
  Identification: how do we find a block in cache?
  Replacement: what to kick out to make room in cache?
  Write policy: What do we do about stores?
Key: Optimize the
average memory
access latency

## Slide 8: Memory Locality
A “typical” program has a lot of locality in memory references
  typical programs are composed of “loops”
Temporal: A program tends to reference the same memory location many times and all within a small window of time
Spatial: A program tends to reference a cluster of memory locations at a time
  most notable examples:
    1. instruction memory references
    2. array/data structure references

## Slide 9: Review questions
Memory addresses A, A+1, A+2, A+3, A+4
  Spatial locality or temporal locality?:
  Spatial locality
Memory addresses A, B,C, A,B,C,A,B,C
  Spatial locality or temporal locality?
  Temporal locality

## Slide 10: Cache Basics: A Layman View
Consider a library in law dept.: many books, each 100 pages.
Pages identified with [BOOKNAME][PAGENUM]
eg. MYBOOK64, OLDBOOK75, FINES88
We have a shelf that can store 2600 pages or 26 Books
How to organize this shelf?

## Slide 11: Cache Basics: A Layman View
Perhaps we want to keep books instead of individual pages  -Less book-keeping overhead
-Likely we read many pages from same book
26 Books. Need to check quickly if book in my shelf
How about partitioning the shelf? Hashing based on first char
What is the problem? Can’t hold two books starting with “A”
How about below: 13 bins (each with two places  flexibility)
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
A or B
Y or Z

## Slide 12: Cache Basics
Cache consists of block-sized lines
  Line size typically power of two
  Typically 16 to 256 bytes in size
Example
  Suppose block size is 256 bytes
    Lowest eight bits determine offset within block
  Read data at address A=0xFADEDACE
  The block address is 0xFADEDA,
  Byte in block is 0xCE
MSB
LSB
Block size

## Slide 13: Cache Placement
Placement
  Which memory blocks are allowed into which cache lines
Placement Policies
  Direct mapped (block can go to only one line)
  Fully Associative (block can go to any line)
  Set-associative (block can go to one of N lines)
    E.g., if N=4, the cache is 4-way set associative
    Other two policies are extremes of this (E.g., if N=1 we get a direct-mapped cache)

## Slide 14: Cache Identification
When address referenced, need to
  Find whether its data is in the cache
  If it is, find where in the cache
  This is called a cache lookup
Each cache line must have
  A valid bit (1 if line has data, 0 if line empty)
    We also say the cache line is valid or invalid
  A tag to identify which block is in the line (if line is valid)

## Slide 15: Index
dex
Index
TAG
Block offset
TAG
TAG
=
=
HIT
YES
YES
Data
Logic
Pop quiz: Why is index typically the least significant bits (LSBs) and not MSBs

## Slide 16: Parallel/Serial TAG and Data Array Access
Synthesis lecture series: microarchitecture

## Slide 17: Cache Replacement
Need a free line to insert new block
  Which block should we kick out?
Several strategies
  Random (randomly selected line)
  FIFO (line that has been in cache the longest)
  LRU (least recently used line)
  LRU Approximations (Pseudo LRU)

## Slide 18: Implementing LRU
Have “time-stamp” with each line  Expensive
Maintain a LRU “stack”
  Ordered list with MRU line on top, LRU line on bottom
  On a hit, remove the line from list and put on top of stack
  For eviction, select line from bottom
Stack Algorithm still needs Log2(Assoc) bits per line
LRU approximations: Clock (1-bit LRU), NMRU, Tree etc.

## Slide 19: Review questions-II
Here is a series of address references given as word address: 1,4,8,5,20,17,19,56,9,11,4,4,3,5,6,9,17. Assuming a direct-mapped cache with 16 one-word blocks that is initially empty, label each reference in the list as a hit or miss and show the final contents of the cache.
1%16 =1
4%16 = 4
8%16 =8
5%16 =5
20%16 = 4
17%16 = 1
19%16 =3
56%16 = 8
9%16 =9
11%16 =11
4%16 = 4
4% 16 = Hit
3 % 16 = 3
5%16 = 5 Hit
6%16 = 6
9%16 = 9 Hit
17%16 =1 Hit
0 | 
1 | 1 17
2 | 
3 | 19 3
4 | 4 20 4
5 | 5
6 | 6
7 | 
8 | 8 56
9 | 9
10 | 
11 | 11 43
12 | 
13 | 
14 | 
15 | 

## Slide 20: Write Policy
Do we allocate cache lines on a write?
  Write-allocate
    A write miss brings block into cache
  No-write-allocate
    A write miss leaves cache as it was
  Pros and cons?
    Depends on temporal locality
Do we update memory on writes?
  Write-through
    Memory immediately updated on each write
  Write-back
    Memory updated when line replaced

## Slide 21: Write Through/Write Back
PROC
CACHE
MEM
PROC
CACHE
MEM
  Write-through
  Write-back
replacement

## Slide 22: Write-Back Caches
Need a Dirty bit for each line (stored in the Tag!)
  A dirty line has more recent data than memory
Line starts as clean (not dirty)
Line becomes dirty on first write to it
  Memory not updated yet, cache has the only up-to-date copy of data for a dirty line
Replacing a dirty line
  Must write data back to memory (write-back)

## Slide 23: Tag Storage
Any information related to cache other than data is stored in the tag storage.
Not only tag bits, information for replacement, dirty bits (if we need), valid bit
(in the future, cache coherence state information)

## Slide 24: TAG
Offset: Byte offset in block
Index: Which set in the cache is the block located
Tag: need to match address tag in cache
Set: Group of blocks corresponding to same index
MSB
LSB
Offset
Index
TAG
Data
address

## Slide 25: Cache Performance
Miss rate
  Fraction of memory accesses that miss in cache
  Hit rate = 1 – miss rate
Average memory access time
  AMAT = hit time + miss rate * miss penalty

## Slide 26: Improving Cache Performance
AMAT = hit time + miss rate * miss penalty
  Reduce miss penalty
  Reduce miss rate
  Reduce hit time

## Slide 27: Improving Cache Performance (2)
Memory latency = 100 cycles
16KB cache, 3 cycle latency, 85% hit rate
What’s the baseline AMAT?
= 3+100*0.15 = 18
What’s the best way to reduce latency?
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  = 1+ 100*0.25 = 26
  Larger 32KB cache: 4 cycle latency, 90% hit rate
  = 4 + 100*0.1 = 14

## Slide 28: Reducing Cache Miss Penalty (1)
Multilevel caches
  Very Fast, small Level 1 (L1) cache
  Fast, not so small Level 2 (L2) cache
  May also have slower, large L3 cache, etc.
Why does this help?
  Miss in L1 cache can hit in L2 cache, etc.
    AMAT = HitTimeL1+MissRateL1MissPenaltyL1
    MissPenaltyL1= HitTimeL2+MissRateL2MissPenaltyL2
    MissPenaltyL2= HitTimeL3+MissRateL3MissPenaltyL3

## Slide 29: Multi-Level Caches
Memory latency = 100 cycles
16KB L1 cache, 3 cycle latency, 85% hit rate
Use two levels of caching
  Smaller 8KB cache: 1 cycle latency, 75% hit rate
  Larger 128KB cache: 6 cycle latency, 60% hit rate
Exclusion Property
  If block is in L1 cache, it is never in L2 cache
  Saves some L2 space
Inclusion Property
  If block A is in L1 cache, it must also be in L2 cache

## Slide 30: Kinds of Cache Misses
The “3 Cs”
  Compulsory: have to have these
    Miss the first time each block is accessed
  Capacity: due to limited cache capacity
    Would not have them if cache size was infinite
  Conflict: due to limited associativity
    Would not have them if cache was fully associative

## Slide 31: Reducing Cache Miss Rate (2)
Larger blocks
  Helps if there is more spatial locality

## Slide 32: Reducing Cache Miss Rate (3)
Larger caches
  Fewer capacity misses, but longer hit latency!
Higher associativity
  Fewer conflict misses, but longer hit latency!
  … need to work through AMAT equations to figure out which is better

## Slide 33: Review question
A computer has an 8KB write-through cache. Each cache block is 64 bits, the cache is 4-way set associative and uses the true LRU replacement policy. Assume a 24-bit address space and byte-addressable memory. How big (in bits) is the tag store