## Slide 1: ECE3056A Architecture, Concurrency, Energy Lecture: GPU Architectures
Slides derived from Prof. Onur Mutlu (CMU)

## Slide 2: Course Grade Thus Far (Out of 80pts)
Max: 93.1 Mean: 71.3 Median: 74.5
Chart: 
Range | Students | Grade
80+ | 25 | A+
72-80 | 11 | A
64-72 | 10 | B
56-64 | 7 | C
48-56 | 6 | ??
<48 | 4 | F

## Slide 3: Slicing and Dicing the Scores
Chart: 
| Lab1Eff | Lab2Eff | Lab3Eff | Lab4Eff | LabOverall
Avg | 88.5913 | 69.6651 | 76.1825 | 89.0857 | 80.8812
Median | 93.5 | 87.9 | 92.8 | 100 | 93.55
Chart: 
| Midterm1 | Midterm2 | MidtermOverall
Avg | 84.3889 | 83.6349 | 84.0119
Median | 86 | 85 | 85.5
Chart: 
| Ectotal | Hwtotal | Participation | Sum(15)
Avg | 5.1397 | 3.6508 | 1 | 9.7905
Median | 6 | 4 | 1 | 11

## Slide 4: VECTOR Processors

## Slide 5: Vector Processors
A vector is a one-dimensional array of numbers
Many scientific/commercial programs use vectors
    for (i = 0; i<=49; i++)
    C[i] = (A[i] + B[i]) / 2
A vector processor is one whose instructions operate on vectors rather than scalar (single data) values
Basic requirements
  Need to load/store vectors  vector registers (contain vectors)
  Need to operate on vectors of different lengths  vector length register (VLEN)
  Elements of a vector might be stored apart from each other in memory  vector stride register (VSTR)
    Stride: distance between two elements of a vector

## Slide 6: Vector Processors (II)
A vector instruction performs an operation on each element in consecutive cycles
  Vector functional units are pipelined
  Each pipeline stage operates on a different data element
Vector instructions allow deeper pipelines
  No intra-vector dependencies  no hardware interlocking within a vector
  No control flow within a vector
  Known stride allows prefetching of vectors into cache/memory

## Slide 7: Vector Processor Advantages
+ No dependencies within a vector
  Pipelining, parallelization work well
  Can have very deep pipelines, no dependencies!
+ Each instruction generates a lot of work
  Reduces instruction fetch bandwidth
+ Highly regular memory access pattern
  Interleaving multiple banks for higher memory bandwidth
  Prefetching
+ No need to explicitly code loops
  Fewer branches in the instruction sequence

## Slide 8: Vector Registers
Each vector data register holds N M-bit values
Vector control registers: VLEN, VSTR, VMASK
Vector Mask Register (VMASK)
  Indicates which elements of vector to operate on
  Set by vector test instructions
    e.g., VMASK[i] = (Vk[i] == 0)
Maximum VLEN can be N
  Maximum number of elements stored in a vector register
V0,0
V0,1
V0,N-1
V1,0
V1,1
V1,N-1
M-bit wide
M-bit wide

## Slide 9: Vector Machine Organization (CRAY-1)
CRAY-1
Russell, “The CRAY-1 computer system,” CACM 1978.
Scalar and vector modes
8 64-element vector registers
64 bits per element
16 memory banks
8 64-bit scalar registers
8 24-bit address registers

## Slide 10: Graphics Processing Units SIMD not Exposed to Programmer (SIMT)

## Slide 11: High-Level View of a GPU

## Slide 12: Concept of “Thread Warps” and SIMT
Warp: A set of threads that execute the same instruction (on different data elements)  SIMT (Nvidia-speak)
All threads run the same kernel
Warp: The threads that run lengthwise in a woven fabric …
Thread Warp 3
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar
Thread
W
Scalar
Thread
X
Scalar
Thread
Y
Scalar
Thread
Z
Common PC
SIMD Pipeline
In SIMD, you need to specify the data array + an instruction (on which to operate the data on) + THE INSTRUCTION WIDTH. Eg: You might want to add 2 integer arrays of length 16, then a SIMD instruction would look like (cooked up instruction) add.16 arr1 arr2 However, SIMT doesn't bother about the instruction width. So, essentially, you could write the above example as: arr1[i] + arr2[i] and then launch as many threads as the length of the array, as you want. Note that, if the array size was, let us say, 32, then SIMD EXPECTS you to explicitly call two such 'add.16' instructions! Whereas, this is not the case with SIMT.

## Slide 13: Loop Iterations as Threads
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time
Slide credit: Krste Asanovic

## Slide 14: SIMT Memory Access
Same instruction in different threads uses thread id to index and access different data elements
Let’s assume N=16, blockDim=4  4 blocks
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
+
+
+
+
+
Slide credit: Hyesoon Kim

## Slide 15: Sample GPU SIMT Code (Simplified)
for (ii = 0; ii < 100; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code
Slide credit: Hyesoon Kim

## Slide 16: Sample GPU Program (Less Simplified)
Slide credit: Hyesoon Kim

## Slide 17: Latency Hiding with “Thread Warps”
Warp: A set of threads that execute the same instruction (on different data elements)
Fine-grained multithreading
  One instruction per thread in pipeline at a time (No branch prediction)
  Interleave warp execution to hide latencies
Register values of all threads stay in register file
No OS context switching
Memory latency hiding
  Graphics has millions of pixels
Decode
R
F
R
F
R
F
A
L
U
A
L
U
A
L
U
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Miss?
Warps accessing
memory hierarchy
Thread Warp 3
Thread Warp 8
Writeback
Warps available
for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline
Slide credit: Tor Aamodt
Notes: With a large number of shader threads multiplexed on the same execution re- sources, our architecture employs fine-grained multithreading where individual threads are interleaved by the fetch unit to proactively hide the potential latency of stalls before they occur. As illustrated by Figure, warps are issued fairly in a round-robin queue. When a thread is blocked by a memory request, shader core simply removes that thread’s warp from the pool of “ready” warps and thereby allows other threads to proceed while the memory system processes its request.
With a large number of threads (1024 per shader core) interleaved on the same pipeline, FGMT effectively hides the latency of most memory operations since the pipeline is occupied with instructions from other threads while memory operations complete. also hides the pipeline latency so that data bypassing logic can potentially be omitted to save area with minimal impact on performance. simplify the dependency check logic design by restricting each thread to have at most one instruction running in the pipeline at any time.

## Slide 18: Warp-based SIMD vs. Traditional SIMD
Traditional SIMD contains a single thread
  Lock step
  Programming model is SIMD (no threads)  SW needs to know vector length
  ISA contains vector/SIMD instructions
Warp-based SIMD consists of multiple scalar threads executing in a SIMD manner (i.e., same instruction executed by all threads)
  Does not have to be lock step
  Each thread can be treated individually (i.e., placed in a different warp)  programming model not SIMD
    SW does not need to know vector length
    Enables memory and branch latency tolerance
  ISA is scalar  vector instructions formed dynamically
  Essentially, it is SPMD programming model implemented on SIMD hardware

## Slide 19: SPMD
Single procedure/program, multiple data
  This is a programming model rather than computer organization
Each processing element executes the same procedure, except on different data elements
  Procedures can synchronize at certain points in program, e.g. barriers
Essentially, multiple instruction streams execute the same program
  Each program/procedure can 1) execute a different control-flow path, 2) work on different data, at run-time
  Many scientific applications programmed this way and run on MIMD computers (multiprocessors)
  Modern GPUs programmed in a similar way on a SIMD computer

## Slide 20: Branch Divergence Problem in Warp-based SIMD
SPMD Execution on SIMD Hardware
  NVIDIA calls this “Single Instruction, Multiple Thread” (“SIMT”) execution
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B
C
D
E
F
A
G
Slide credit: Tor Aamodt

## Slide 21: Control Flow Problem in GPUs/SIMD
GPU uses SIMD pipeline to save area on control logic.
  Group scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths.
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt

## Slide 22: Branch Divergence Handling (I)
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Slide credit: Tor Aamodt

## Slide 23: What About Memory Divergence?
Modern GPUs have caches
Ideally: Want all threads in the warp to hit (without conflicting with each other)
Problem: One thread in a warp can stall the entire warp if it misses in the cache.
Need techniques to
  Tolerate memory divergence
  Integrate solutions to branch and memory divergence

## Slide 24: NVIDIA GeForce GTX 285
NVIDIA-speak:
  240 stream processors
  “SIMT execution”
Generic speak:
  30 cores
  8 SIMD functional units per core
Slide credit: Kayvon Fatahalian

## Slide 25: NVIDIA GeForce GTX 285 “core”
…
= instruction stream decode
= SIMD functional unit, control
shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for fragment contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 26: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp)
Up to 32 warps are simultaneously interleaved
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B

## Slide 27: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
There are 30 of these things on the GTX 285: 30,720 threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well