## Slide 1: Working of Two Level Predictor
Moinuddin K Qureshi

## Slide 2: An Example Loop
Consider the following loop executed indefinitely
  for(i=0; i<4; i++)
  array[i] += x;
The above loop gets assembled to something like this:
LD R0, PTR
ADD R0,R0,X
ST R0, PTR
PTR++
CTR--
BNEZ TOP ( This branch TTTN TTTN TTTN …)

## Slide 3: The Loop (First Time, i=1)
T T T N T T T N T T T N …
0 0 0
00
00
00
00
00
00
00
00
History Reg (HR)
PHT
Prediction : Index[000] = 00  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
0 0 1
01
Encodings:
Taken=1,
Not Taken=0
NT

## Slide 4: The Loop (First Time, i=2)
00
T T T N T T T N T T T N …
0 0 1
00
00
00
00
00
00
History Reg (HR)
PHT
Prediction : Index[001] = 00  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
0 1 1
01
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 5: The Loop (First Time, i=3)
011
T T T N T T T N T T T N …
0 1 1
00
00
00
00
00
00
History Reg (HR)
PHT
Prediction : Index[011] = 00  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 1 1
01
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 6: The Loop (First Time, i=4)
011
T T T N T T T N T T T N …
1 1 1
00
01
00
00
00
00
History Reg (HR)
PHT
Prediction : Index[111] = 00  Pred Not Taken (Right)
Update: Both PHT[index] and HR (Shift HR and insert 0)
1 1 0
00
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 7: The Loop (Second Time, i=1)
011
T T T N T T T N T T T N …
1 1 0
00
01
00
00
00
00
History Reg (HR)
PHT
Prediction : Index[110] = 00  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 0 1
01
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 8: The Loop (Second Time, i=2)
011
T T T N T T T N T T T N …
1 0 1
00
01
00
00
01
00
History Reg (HR)
PHT
Prediction : Index[101] = 00  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
0 1 1
01
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 9: The Loop (Second Time, i=3)
011
T T T N T T T N T T T N …
0 1 1
00
01
00
01
01
00
History Reg (HR)
PHT
Prediction : Index[011] = 00  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 1 1
10
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 10: The Loop (Second Time, i=4)
011
T T T N T T T N T T T N …
1 1 1
00
10
00
01
01
00
History Reg (HR)
PHT
Prediction : Index[111] = 00  Pred Not Taken (Right)
Update: Both PHT[index] and HR (Shift HR and insert 0)
1 1 0
00
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 11: The Loop (Third Time, i=1)
011
T T T N T T T N T T T N …
1 1 0
00
10
00
01
01
00
History Reg (HR)
PHT
Prediction : Index[110] = 01  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 0 1
10
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 12: The Loop (Third Time, i=2)
011
T T T N T T T N T T T N …
1 0 1
00
10
00
01
01
00
History Reg (HR)
PHT
Prediction : Index[101] = 01  Pred Not Taken (Wrong)
Update: Both PHT[index] and HR (Shift HR and insert 1)
0 1 1
10
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 13: The Loop (Third Time, i=3)
011
T T T N T T T N T T T N …
0 1 1
00
10
00
01
10
00
History Reg (HR)
PHT
Prediction : Index[011] = 10  Pred Taken (Right)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 1 1
11
Encodings:
Taken=1,
Not Taken=0
T
01

## Slide 14: The Loop (Third Time, i=4)
011
T T T N T T T N T T T N …
1 1 1
00
11
00
01
10
00
History Reg (HR)
PHT
Prediction : Index[111] = 00  Pred Not Taken (Right)
Update: Both PHT[index] and HR (Shift HR and insert 0)
1 1 0
00
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 15: The Loop (Fourth Time, i=1)
011
T T T N
1 1 0
00
11
00
01
10
00
History Reg (HR)
PHT
Prediction : Index[110] = 10  Pred Not Taken (Correct!)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 0 1
11
Encodings:
Taken=1,
Not Taken=0
T
01

## Slide 16: The Loop (Fourth Time, i=2)
011
T T T N
1 0 1
00
11
00
01
11
00
History Reg (HR)
PHT
Prediction : Index[101] = 01  Pred NT (Wrong, but fixed )
Update: Both PHT[index] and HR (Shift HR and insert 1)
0 1 1
10
Encodings:
Taken=1,
Not Taken=0
T
01

## Slide 17: The Loop (Fourth Time, i=3)
011
T T T N
0 1 1
00
11
00
01
10
00
History Reg (HR)
PHT
Prediction : Index[011] = 11 Pred Taken (Correct!)
Update: Both PHT[index] and HR (Shift HR and insert 1)
1 1 1
11
Encodings:
Taken=1,
Not Taken=0
T
01

## Slide 18: The Loop (Fourth Time, i=4)
011
T T T N
1 1 1
00
11
00
01
10
00
History Reg (HR)
PHT
Prediction : Index[111] = 00  Pred Not Taken (Right)
Update: Both PHT[index] and HR (Shift HR and insert 0)
1 1 0
00
Encodings:
Taken=1,
Not Taken=0
NT
01

## Slide 19: For Subsequent iterations
011
T T T N
1 1 1
00
11
00
11
11
00
History Reg (HR)
PHT
Prediction Accuracy becomes 100%
Counters that matter gets saturated to either 11 or 00
00
Encodings:
Taken=1,
Not Taken=0
NT
01
T
T
T
1 1 0
1 0 1
0 1 1

## Slide 20: Extra Credit: Evaluating Branch Predictors (2 points of your grade)
Your job is to measure the prediction accuracy of the following predictors over the three traces A, B, and C:
Never Taken (already implemented)
Always Taken (already implemented)
Last Time (already implemented, use as base)
Two Bit Counter (need to implement)
Two Level Predictor (need to implement)
Complete the four functions in predictor.cc
Run the traces on your predictors. Submit Report.pptx & predictor.cc
Needs about 25 lines of code (perhaps the easiest extra credit)