## Slide 1: ECE3056: Virtual Memory
Prof. Moinuddin Qureshi

## Slide 2: Virtual Memory/Physical Memory
Programmer’s view: virtual memory space
Actual hardware’s view: Physical memory space
In hardware: translation from virtual address to physical address
Virtual Address
Virtual Page Number
Page Offset
Physical Frame Num
Page Offset
Physical Address
Translation
Protection check!
Read/write, kernel/user?

## Slide 3: Virtual Memory: Get by with Less
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
Lets say user space is 16 pages (0-F), but we have only four physical pages
3 | X | X | X | X | 0 | X | X | 2 | 1 | X | X | X | X | X | X
At any time only four pages valid (mapped to physical pages)
Access to invalid page causes page fault (evict a page and reallocate)
Say we access Page F and replacement policy evicts Page 8 (frame 2 is free!)
3 | X | X | X | X | 0 | X | X | X | 1 | X | X | X | X | X | 2

## Slide 4: Virtual Memory: Share Physical Mem
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
Lets say we have two programs (P1 and P2)
Virtual Memory allows each application an illusion that it has entire memory
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
P1
P2
7 | X | X | X | X | 1 | X | X | 6 | 3 | X | X | X | X | 0 | X
2 | X | X | X | X | 4 | X | X | X | X | X | X | X | X | 5 | X
P1
P2
Lets say we have 8 physical frames (5 given to P1 and 3 to P2)

## Slide 5: Need for Translation
Virtual Address
Virtual Page Number
Page Offset
Page
Table
Main
Memory
Physical
Address
0xFC51908B
0x00152
0xFC519
0x0015208B

## Slide 6: CPU Memory Access
Program deals with virtual addresses
  “Load R1 = 0[R2]”
On memory instruction
  Compute virtual address (0[R2])
  Compute virtual page number
  Compute physical address of VPN’s page table entry
  Load* mapping
  Compute physical address
  Do the actual Load* from memory
Could be more depending
On page table organization

## Slide 7: Impact on Performance?
Every time you load/store, the CPU must perform two (or more) accesses!
Even worse, every fetch requires translation of the PC!
Observation:
  Once a virtual page is mapped into a physical page, it’ll likely stay put for quite some time

## Slide 8: Idea: Caching!
Not caching of data, but caching of translations
0K
4K
8K
12K
Virtual
Addresses
0K
4K
8K
12K
16K
20K
24K
28K
Physical
Addresses
8
16
0
20
4
4
12
X
VPN 8
PPN 16
TLB also has protection bits, R/W, kernel/user information

## Slide 9: Translation Cache: TLB
TLB = Translation Look-aside Buffer
TLB
Virtual
Address
Cache
Data
Physical
Address
Cache
Tags
Hit?
If TLB hit, no need to
do page table lookup
from memory
Note: data cache
accessed by physical
addresses now
Cache permissions
as well

## Slide 10: Multi-Level Page Tables
Level 1
Level 2
Page Offset
Physical Page Number
Virtual Page Number
Say each PTE entry is 8B, what is the size of Page Table for 32 bit address space?
How about 64-bit address space?

## Slide 11: TLB Miss?
Software solution
  Generate an exception
  O/S
Hardware solution
  Hardware page walker
  TLB miss handler
  Needs to know TLB miss in advance

## Slide 12: PAPT Cache
So far we haven’t differentiate physical and virtual addresses so much
Previous slide showed Physically-Addressed Physically-Tagged cache
  Sometimes called PIPT (I=Indexed)
Con: TLB lookup and cache access serialized
  Caches already take > 1 cycle
Pro: cache contents valid so long as page table not modified

## Slide 13: Virtually Addressed Cache
Virtual
Address
Cache
Data
Cache
Tags
Hit?
Pro: latency – no need to check TLB
Con: Cache must be flushed on process change
(VIVT: vitually
indexed,
virtually tagged)
TLB
On Cache
Miss
Physical
Address
To L2

## Slide 14: Virtually Indexed Physically Tagged
Virtual
Address
Cache
Data
Cache
Tags
Hit?
Pro: latency – TLB parallelized
Pro: don’t need to flush $ on process swap
Con: Limit on cache indexing (can only use bits not from the VPN/PPN)
TLB
Physical Address
=
Physical Tag
Big page size
can help here

## Slide 15: Virtual Index Physical Tag
Virtual Address
Virtual Page Number
Page Offset
Physical Frame Num
Page Offset
Physical Address
TAG
B. offset
Index
TAG
B. offset
Index
Good
BAD

## Slide 16: Some Solutions to the Synonym Problem
Limit cache size to page size times associativity
  get index from page offset
On a write, search all possible indices that can contain the same physical block, and update/invalidate
  Used in Alpha 21264, MIPS R10K
Restrict page placement in OS
  make sure index(VA) = index(PA)
  Called page coloring
  Used in many SPARC processors

## Slide 17: Programming
Programming: Virtual or Physical ?
Data sharing in parallel programming
  Virtual or Physical ?
  Different VAs need to mapped to the same PA
  Virtual-index-physical-tag Cache
  VA1 = PA1 = {tag1, index1, offset1}
  VA2 = PA1 = {tag1, index2, offset1}